## Slide 1: RIPPLE CARRY ADDER
Department of computer science AVAH Arts and Science college, kulupa

## Slide 2
Ripple Carry Adder is a combinational logic circuit.
It is used for the purpose of adding two n-bit binary numbers.
It requires n full adders in its circuit for adding two n-bit binary numbers.
It is also known as n-bit parallel adder.

## Slide 3
A ripple carry adder is a logic circuit in which the carry-out of each full adder is the carry in of the succeeding next most significant full adder.
It is called a ripple carry adder because each carry bit gets rippled into the next stage.

## Slide 4
In Mathematics, any two 4-bit binary numbers A3A2A1A0 and B3B2B1B0 are added as shown below-

## Slide 5
Using ripple carry adder, this addition is carried out as shown by the following logic diagram-

## Slide 6
The two 4-bit numbers are 0101 (A3A2A1A0) and 1010 (B3B2B1B0).
These numbers are to be added using a 4-bit ripple carry adder.

## Slide 7
4-bit Ripple Carry Adder carries out the addition as explained in the following stages-
Stage-01:
When Cin is fed as input to the full Adder A, it activates the full adder A.
Then at full adder A, A0 = 1, B0 = 0, Cin = 0.
Full adder A computes the sum bit and carry bit as-

## Slide 8
Calculation of S0–
S0 = A0 ⊕ B0 ⊕ Cin
S0 = 1 ⊕ 0 ⊕ 0
S0 = 1
Calculation of C0–
C0 = A0B0 ⊕ B0Cin ⊕ CinA0
C0 = 1.0 ⊕ 0.0 ⊕ 0.1
C0 = 0 ⊕ 0 ⊕ 0
C0 = 0

## Slide 9
Stage-02:
When C0 is fed as input to the full adder B, it activates the full adder B.
Then at full adder B, A1 = 0, B1 = 1, C0 = 0.
Full adder B computes the sum bit and carry bit as-
Calculation of S1–
  S1 = A1 ⊕ B1 ⊕ C0
  S1 = 0 ⊕ 1 ⊕ 0
  S1 = 1
Calculation of C1–
  C1 = A1B1 ⊕ B1C0 ⊕ C0A1
  C1 = 0.1 ⊕ 1.0 ⊕ 0.0
  C1 = 0 ⊕ 0 ⊕ 0
  C1 = 0

## Slide 10
Stage-03:
When C1 is fed as input to the full adder C, it activates the full adder C.
Then at full adder C, A2 = 1, B2 = 0, C1 = 0.
Full adder C computes the sum bit and carry bit as-
Calculation of S2–
  S2 = A2 ⊕ B2 ⊕ C1
  S2 = 1 ⊕ 0 ⊕ 0
  S2 = 1
Calculation of C2–
  C2 = A2B2 ⊕ B2C1 ⊕ C1A2
  C2 = 1.0 ⊕ 0.0 ⊕ 0.1
  C2 = 0 ⊕ 0 ⊕ 0
  C2 = 0

## Slide 11
Stage-04:
When C2 is fed as input to the full adder D, it activates the full adder D.
Then at full adder D, A3 = 0, B3 = 1, C2 = 0.
Full adder D computes the sum bit and carry bit as-
Calculation of S3–
  S3 = A3 ⊕ B3 ⊕ C2
  S3 = 0 ⊕ 1 ⊕ 0
  S3 = 1
Calculation of C3–
  C3 = A3B3 ⊕ B3C2 ⊕ C2A3
  C3 = 0.1 ⊕ 1.0 ⊕ 0.0
  C3 = 0 ⊕ 0 ⊕ 0
  C3 = 0
  Thus finally,
  Output Sum = S3S2S1S0 = 1111
  Output Carry = C3 = 0

## Slide 12: Disadvantages of Ripple Carry Adder-
Ripple Carry Adder does not allow to use all the full adders simultaneously.
Each full adder has to necessarily wait until the carry bit becomes available from its adjacent full adder.
This increases the propagation time.
Due to this reason, ripple carry adder becomes extremely slow.
This is considered to be the biggest disadvantage of using ripple carry adder.

## Slide 13
THANK YOU